## Slide 1: GMEM：面向领域加速器的通用内存管理
华为操作系统技术专家
朱维希
2023.10

## Slide 2: The golden age of accelerators
Powered by Accelerators

## Slide 3: The heart of openEuler's OS for AI
GMEM: history and future
Originated from my PhD study at Rice Univ,
inspired by
a. Micro-arch opportunities;
b. OS design principles
Academic literature available:
GMEM: Generalized Memory Management for Peripheral Devices (arXiv:2310.12554 [cs.OS])
Prof. Scott Rixner
Prof. Alan L. Cox
Linux-based version soon available in openEuler 23.09 in early Oct, 2023

## Slide 4
Memory is the core of AI Infra
AI/heterogeneous applications require
  CPU coordination
  Large memory capacity
  Fast memory allocation
  High memory utilization
However, the reality...
  Poor programmability : CPU buffer? GPU buffer?
  OOM (Out-of-memory) : small HBM capacity
  Slow “malloc/free” : not reinvented well
  Memory Fragmentation : failed to malloc 500MB with 10GB free HBM!
4TB/s & 96GB

## Slide 5: The cost of reinventing “malloc”
Device “Malloc” (#LoC) | User-level “malloc” | User-level swapping | Total
PyTorch | 3,650 | 2,509 | ~6K
TensorFlow | 2,228 | 1,557 | ~4K
tc/je/ptmalloc
AI framework
CPU Apps
AI Apps
Do they work well?
Latency comparison (small sizes):
PyTorch vs. jemalloc:
1000ns vs. 300ns
3x slower!

## Slide 6: The cost of reinventing mm subsystem
Device MM (#LoC) | Core Device MM | Kernel-level Swapping | Total
Nvidia | ~34K | ~70K | ~104K
AMD | ~14K | N/A | ~14K
Huawei Ascend | ~30K | N/A | ~30K
mmap/sbrk/
madvise
OS
cudaMalloc/...
Device driver
Linux core mm: 80K LoC
FreeBSD core mm: 30K LoC
Bugs?
System overhead?
Memory fragmentation?

## Slide 7: Motivation of GMEM
Stop people from further reinventing the wheel
  No more “malloc” for GPU, TPU, etc.
  No more mm systems for device drivers
Enhanced programmability
  Unified virtual address space / User-guided memory advice
  Device memory oversubscription
Better memory service
  Faster malloc/free speed
  Higher memory utilization

## Slide 8
Because MM subsystems are no different!
  1. Virtual address allocation/deallocation
  2. Physical address allocation/deallocation
  3. VA-PA address mapping management
  4. Physical data preparation (zero, copy, DMA)
Invoke hardware-specific handling
Why can the OS manage *ANY*
accelerator’s memory?

## Slide 9: A high-level view of GMEM design
Only provide high-level APIs
Decouple low-level MMU handling
3. Require registering MMU functions
4. Coordinate multiple page tables within each address space

## Slide 10: Why not Linux HMM?
TL;DR
HMM helps driver-Linux mm collaboration but cannot prevent reinventing one.
mmap, madvise
Linux MM
malloc
x86
arm
4-layer page walk functions
Implement your own accelerator’s MM!
handle_mm_fault: a better version
of get_user_pages)
MMU notifiers: triggered by
Linux MM events

## Slide 11: Or just cache-coherent bus?
GMEM makes the OS aware of accelerator nodes
  Data by default is preferably faulted on HBM
  Provides memory hints for user’s proactive prefetch
  Remote access / fault driven migration?
DDR
HBM
CPU
Accelerator
CXL/NVLink/…
  IBM P9-Volta bug:
  OS falsely populates DDR pages when handling GPU page faults

## Slide 12: GMEM implementation
Unified virtual address space
  mm_struct points to CPU, accelerator page table
Per-process logical page table for mapping coherence
  GMEM maintains a coherent view of memory
Invoking MMU functions
  Accelerator-specific
VMA management
MM struct
CPU page table
walker
Buddy allocator
Accelerator #1 attached
Accelerator #2 attached
Logical page table
MMU functions
MMU functions
GMEM mapping coherence

## Slide 13: Key features of GMEM
Enhanced programmability
  CPU and accelerator share virtual pointers
  Transparent memory oversubscription
  Waive OOM (out-of-memory) issue
Debloat redundant mm code
  Waive driver’s mm development
  Waive App’s malloc development
User-guided heterogeneous memory hints
  Proactive data prefetches
  Easy comp/comm overlapping

## Slide 14
GMEM Evaluation

## Slide 15: Programmability
Stream 1
Stream 2
Matmul kernel
Prefetch(A)
Prefetch(B)
Prefetch(C)
Synchronize (Barrier)
Easy comp/comm overlapping:
*Correctness is guaranteed by GMEM’s concurrent page fault mechanism.
Malloc pointers are sharable between CPU and accelerators.

## Slide 16: MM/Malloc basic performance
User-level | Avg. Latency
malloc (GMEM) | 300ns
PyTorch’s “malloc” | 1000ns
3x faster
Memory-sensitive Apps (redis, gcc) has <1% perf penalty with GMEM’s refactoring Linux MM

## Slide 17: OS code debloating
MM Systems | # LoC
Ascend NPU driver | 30,000
GMEM-based NPU driver | 30 (calling GMEM API) + 2000 (underlying MMU functions)
90% less code

## Slide 18: Memory defragmentation
Protein folding prediction (an alphafold variant):
Problem size: 25% larger
End-to-end inference speed: 20%~40% (due to faster kernel compilation)
We are applying GMEM to enhance LLM inference throughput, stay tuned!

## Slide 19: Transparent memory oversubscription
A 32GB NPU card was able to train a 52B LLM model,
with <10 LoC changes in the AI framework,
oversubscribing 1TB DDR, powered by GMEM.

## Slide 20: Conclusions & future work
GMEM solves the wild growth of memory service code
  Accelerator memory management – now Linux MM simply works
  “Malloc” code in AI-platform – now any tc/je/whatever malloc works
The core of AI-infrastructure
  Enhanced programmability: unified virtual address space
  Faster malloc & Higher HBM util.
  Alleviate OOM/Memory fragmentation
  Transparent memory oversubscription
  User-guided memory hints

## Slide 21: Roadmap of open-sourcing
Call for contribution
  Accelerator driver developers
Availability
  Currently: preliminary code available
  openEuler 23.09 (2023-Oct) – source code + documentation
  openEuler 24.03 LTS (2024-Mar) – better extended
Please subscribe openEuler maillist 
  SIG-compute: dev@openEuler.org
  SIG-kernel: kernel@openEuler.org
Notes: Sig组的邮件地址
Kernel组邮件列表

## Slide 22: 谢谢！