## Slide 1: Xen Based GPU Virtualization - VirtIO / Passthrough
Ray Huang (Huang Rui) <ray.huang@amd.com>
CLK - China Linux® Kernel 2023

## Slide 2: Who are we?
Ray Huang - China
  Kernel (GPU, Xen)/QEMU/Xen
Julia Zhang - China
  Mesa 3D (OpenGL, Vulkan)/Virglrenderer/QEMU
Honglei Huang - China
  Mesa Multimedia/Virglrenderer/QEMU/ROCm
Jiqian Chen - China
  Kernel (GPU, Xen)/QEMU/Xen
Pierre-Eric Pelloux-Prayer - France
  Mesa 3D (OpenGL, Vulkan)/Virglrenderer/QEMU
Xenia Ragiadakou - Greece
  Xen/QEMU/Kernel (Xen)
Leo Liu - Canada
  Mesa Multimedia/Virglrenderer
Boyuan Zhang - Canada
  Mesa Multimedia/Virglrenderer
Robert Beckett - United Kingdom
  Mesa 3D (OpenGL, Vulkan)/Virglrenderer/QEMU

## Slide 3: Intention
Automotive Infotainment on AMD
  Multiple Systems (Guest VM) in one Car
  Xen based GPU Virtualization
  3D Graphic and Multimedia hardware acceleration

## Slide 4: Technical Background
VirtIO GPU - Only Virgl
  Virgl is a 3D OpenGL implementation for VirtIO GPU
  Not fully verified on Xen
  No Vulkan support
DOM0 PV on x86 CPU
  PV is using the swiotlb for DMA operations on all PCI devices
  However, in AMD GPU use cases, there are always many large sized buffer mappings as large as Mbytes or Gbytes on the device. Swiotlb is not usable for GPU
PCI Passthrough on PV dom0
  GPU passthrough is a very popular use case for virtualization
  But it only can be mapped into one guest DOMU
  Passthrough is only supported under PV dom0

## Slide 5: New Proposal to improve GPU virtualization on Xen
Graphic stack including OpenGL and Vulkan
  Improve OpenGL support in guest domU
  Add Vulkan support in guest domU
  Steam games and graphic benchmark coverage
Xen PVH dom0 for AMDGPU on x86 CPU
  Support native AMDGPU kernel on dom0
  Support PCIe Passthrough for AMDGPU on PVH dom0
Multiple types of GPUs support in one guest DOMU
  VirtIO GPU and Passthrough GPU transaction together
  Multiple VirtIO GPUs together

## Slide 6: GPU Passthrough on Xen PVH DOM0
Kernel
  Unmask gsi (New for PVH dom0)
    io_apic_write - trap into Xen hypervisor
  Reset Device's state (New for PVH dom0)
    PHYSDEVOP_pci_device_state_reset
QEMU
  Config initialization
    Get real device base info
    Initialize emulated registers
  Map gsi to pirq
    Translate irq to gsi(New for PVH dom0)
    Use gsi to do PHYSDEVOP_map_pirq
  IO Port/Memory Mapping
    XEN_DOMCTL_ioport_mapping and XEN_DOMCTL_memory_mapping
Platform
Xen Hypervisor
Discrete GPU (PCIe)
VBIOS/Firmware
PHYSDEVOP_pci_device_state_reset
vioapic_hwdom_map_gsi
XEN_DOMCTL_memory_mapping
Linux® PVH (DOM0)
QEMU
DOM0 Kernel
xen_pt_realize
LibXL PCI
PCI assignable add / remove
Xen Pciback
unmask_irq
Xen x86 PCI
xen_host_pci_device_get
xen_pt_register_regions
xen_pt_region_update
xc_physdev_map_pirq
xc_domain_memory_mapping
Ubuntu Linux®
(DOMU)
LibDRM
Mesa
Radv
Xserver/Wayland
Kernel
Kernel AMD GPU
DRI Interface/ICD Interface
RadeonSi

## Slide 7: Blob Memory Introduction
Blob Memory Usage
  VirtIO GPU Driver: Virgl / Venus
  AMD Native Driver: RadeonSi / Radv
QEMU on Xen mem-path (No udma-buf on Xen)
  Remove udma-buf to support Xen
Virtual GPU local memory - Blob Memory
  Add local memory in virtual MMIO bar
  Provide the direct memory access like VRAM for virtual GPU
  QEMU/Virglrenderer responds the virtio command to create and map the blob memory from guest virtual MMIO bar
      00:04.0 VGA compatible controller: Red Hat, Inc. Virtio GPU (rev 01) (prog-if 00 [VGA controller])
      Subsystem: Red Hat, Inc. Virtio GPU
      Physical Slot: 4
      Flags: bus master, fast devsel, latency 0, IRQ 32
      Memory at f1000000 (32-bit, prefetchable) [size=8M]
      Memory at f1b74000 (32-bit, non-prefetchable) [size=4K]
      Memory at f1b70000 (64-bit, prefetchable) [size=16K]
      Memory at 200000000 (64-bit, prefetchable) [size=4G]
      Expansion ROM at 000c0000 [disabled] [size=128K]
      Capabilities: <access denied>
      Kernel driver in use: virtio-pci
device_model_args_hvm = ["-display", "sdl,gl=on", "-device", "virtio-vga gl,context_init=true,blob=true,hostmem=4G"]
[ 19.211594] [drm] Host memory window: 0x200000000 +0x100000000
[ 19.211706] [drm] features: +virgl -edid +resource_blob +host_visible
[ 19.211707] [drm] features: +context_init
[ 19.228967] [drm] number of scanouts: 1
[ 19.229092] [drm] number of cap sets: 3

## Slide 8: Blob Memory to Local GPU buffer on Xen
Guest Mesa (Virgl/Venus or Native Context)
  Be able to use blob memory for direct access in the guest instead of command transfer
Guest Kernel
  Expose a MMIO bar in PCI config space for blob memory. (hostmem)
Blob Memory Commands in QEMU
  Provide blob memory commands implementation
Virglrenderer
  Get the host virtual address of local GPU buffer which exposed by DMA-BUF
Xen
  Convert the host virtual address to host physical address to connect it with guest physical address with hypervisor calls
  Only can be used for pining buffer (no eviction) - challenge
Virglrenderer
Virgl Resource
QEMU
virtio-gpu resource
VirtIO GPU PCIe Device
Hostmem (MMIO BAR)
Kernel
AMDGPU Buffer
MemoryRegion
MMAP DMA-BUF
Xen
xc_domain_add_to_physmap_batch
xc_domain_memory_mapping
Host PFN
Guest PFN
VirtIO GPU
Guest Buffer Object
Mapping host buffer to guest
map_hva_to_gpfns

## Slide 9: Virgl and Venus
Platform
APU (integrated GPU) Platform
SBIOS/VBIOS/Firmware
Xen Hypervisor
Ubuntu Linux®
(DOMU)
LibDRM
Mesa
Xserver/Wayland
Kernel
Kernel VirtIO GPU
DRI Interface/ICD Interface
Virgl
Linux® PVH (DOM0)
QEMU
Mesa
Virglrenderer
DOM0 Kernel
LibDRM
Kernel DRM AMDGPU (iGPU)
OpenGL
Vulkan
Vrend context
Vkr context
Virglrenderer cmd
virtio-gpu-virgl cmd
virtio-gpu-virgl blob memory commands
Bring up Venus Support on Xen
  No Vulcan is functional on Xen guest based on VirtIO GPU
  Implement blob memory support with virtio-gpu-virgl in QEMU
  Implement the use case to import a blob resource of external vulkan with OpenGL while egl is not initialized
Virglrenderer
  https://gitlab.freedesktop.org/virgl/virglrenderer/-/merge_requests/1068
Mesa
  https://gitlab.freedesktop.org/mesa/mesa/-/merge_requests/23680
QEMU - Blob Memory
  https://lore.kernel.org/qemu-devel/20230915111130.24064-1-ray.huang@amd.com
Venus

## Slide 10: Virgl Video
Platform
APU (integrated GPU) Platform
SBIOS/VBIOS/Firmware
Xen Hypervisor
Ubuntu Linux® (DOMU)
App (ffmpeg / mpv)
Mesa
Kernel
wayland
VAAPI
EGL
virgl
LibDRM
Kernel VirtIO GPU
Linux® PVH (DOM0)
QEMU
Mesa
Virglrenderer
DOM0 Kernel
LibDRM
Kernel DRM AMDGPU (iGPU)
OpenGL
Vulkan
Vrend context
Vkr context
Virglrenderer cmd
virtio-gpu-virgl cmd
Introduce Virgl Video on Xen
  Support multiple video codec
    Mpeg12/VC1/JEPG/HEVC10bit/VP9
Virgl video corresponding behavior of VM VAAPI in host
  Initial VAAPI when the VM starts.
  Create Vasurface
  Create a true config and context for this decoding in host
  Start the actual decoding process in host while VM calls renderPictures()
Mesa/Virglrenderer
  https://gitlab.freedesktop.org/mesa/mesa/-/merge_requests/22108
  https://gitlab.freedesktop.org/virgl/virglrenderer/-/merge_requests/1068
Virgl Video

## Slide 11: VirtIO Native Context
VirtIO Native Context with AMDGPU on Xen - Coming
  One more straightforward way than Virgl/Venus
  API Forward with Libdrm instead of OpenGL/Vulkan interfaces
  Leverage blob memory with native OpenGL/Vulkan in the guest
  No Mesa running in the host (faster)
Initial the design bases on the work of Bob Clark and refer the corresponding presentation on XDC2022
  https://gitlab.freedesktop.org/mesa/mesa/-/merge_requests/21658
Platform
APU (integrated GPU) Platform
SBIOS/VBIOS/Firmware
Xen Hypervisor
Linux® PVH (DOM0)
QEMU
Virglrenderer
DOM0 Kernel
LibDRM
Kernel DRM AMDGPU (iGPU)
AMDGPU DRM Renderer context
Virglrenderer cmd
virtio-gpu-virgl cmd
virtio-gpu-virgl blob memory commands
No Mesa running in Host dom0
Ubuntu Linux®
(DOMU)
LibDRM
Mesa
Radv
Xserver/Wayland
Kernel
Kernel VirtIO GPU
DRI Interface/ICD Interface
RadeonSI
VirtIO GPU Backend

## Slide 12: dGPU Prime on Native Context
Native context: virtio-GPU + passthrough GPU
Ubuntu Linux® (DOMU)
LibDRM
Mesa
Xserver/Wayland
Kernel
Kernel VirtIO GPU
Kernel AMD GPU
DRI Interface/ICD Interface
RadeonSi
resource
RadeonSi
resource
Others
Other drivers
create render buffer
create display buffer
import
blob create
Two VirtIO GPU
Ubuntu Linux® (DOMU)
LibDRM
Mesa
Xserver/Wayland
Kernel
Kernel VirtIO GPU
Kernel VirtIO GPU
DRI Interface/ICD Interface
Radeonsi
resource
RadeonSi
resource
Others
Other drivers
create render buffer
create display buffer
import
blob
create
blob
create

## Slide 13: OpenGL Comparison between Virgl and Native Context
Test Cases (Unit: FPS) | Histogram | Bare-Metal – Native (RadeonSi) | DOMU – Virgl | DOMU – Native Context (RadeonSi)
CS:GO |  | 70 | 43 (61.43%) | 45 (64.29)
pts/tesseract |  | 123.61 | 58.14 (47.04%) | 107.45 (86.93%)
pts/xonotic |  | 201.77 | 91.51 (45.35%) | 131.11 (64.98)
GFXBench (gl_Manhattan) |  | 121.39 | 88.89 (73.23%) | 118.12 (97.31%)

## Slide 14: Vulkan Comparison between Venus and Native Context
Test Cases(Unit: FPS) | Histogram | Bare-Metal – Native (Radv) | DOMU – Venus | DOMU – Native Context (Radv)
Dota 2 |  | 50.3 | 29.8 (81.02%) | 33.2 (88.86%)
Rise Of The Tomb Raider |  | 23.01 | 16.33 (70.97%) | 22.32 (97.00%)
The Talos Principle |  | 68.7 | 25.3 (36.83%) | 61.0 (88.79%)
GFXBench (vulkan_5_high) |  | 44.60 | 24.96 (55.96%) | 43.94 (98.52%)

## Slide 15: ROCm with VirtIO Native Context - Design Preview
AMD ROCm on guest DOMU - Coming
  Support OpenCL™ over ROCm for virtualization
  Also inspired by virtio native context on graphic design
API Forward for Libhsakmt (Thunk)
  Introduce VirtIO GPU backend in ROCm runtime and OpenCL™ runtime
  Add libhsakmt capacity in QEMU
  Leverage blob memory
  Add libhsakmt renderer in virglrenderer
Platform
APU (integrated GPU) Platform
SBIOS/VBIOS/Firmware
Xen Hypervisor
Ubuntu Linux®
(DOMU)
LibDRM
ROCm Runtime
OpenCL™ Application
Kernel
Kernel VirtIO GPU
VirtIO GPU Backend
OpenCL™ Loader
OpenCL™ Driver
CL Runtime
Address Traction Layer
Linux® PVH (DOM0)
QEMU
Virglrenderer
DOM0 Kernel
Libhaskmt Thunk
Kernel DRM AMDGPU
Libhsakmt Renderer
Virglrenderer cmd
virtio-gpu-virgl cmd
virtio-gpu-virgl blob memory commands
No ROCm running in host DOM0
AMDKFD
Libhsakmt Capset

## Slide 16: The Best is Yet to Come
Continue upstream for the whole solution - On going
Full graphic benchmark verification
Resolve the direct mapping of virtual MMIO bar for QEMU on Xen
  Plan to use an MMU notifier
Implement the approach to enable AMD ROCm compute stack at guest VM with VirtIO
  Support leading AI Frameworks over ROCm for virtualization

## Slide 17: References
Hardware
  AMD Ryzen 4000G Series APUs
  AMD Radeon™ RX 6000 Series GPUs
Repositories
  Kernel - https://git.kernel.org/pub/scm/linux/kernel/git/rui/linux.git/log/?h=upstream-fox-xen
  Xen - https://gitlab.com/huangrui123/xen/-/commits/upstream-for-xen
  QEMU - https://gitlab.com/huangrui123/qemu/-/commits/upstream-for-xen
  Virglrenderer - https://gitlab.freedesktop.org/rui/virglrenderer/-/commits/upstream-for-xen
  Mesa - https://gitlab.freedesktop.org/rui/mesa/-/commits/upstream-for-xen
Upstream is in progress
  Kernel - https://lore.kernel.org/lkml/20230312120157.452859-1-ray.huang@amd.com/
  Xen - https://lore.kernel.org/xen-devel/20230312075455.450187-1-ray.huang@amd.com/
  QEMU - https://lore.kernel.org/qemu-devel/20230312092244.451465-1-ray.huang@amd.com/
  Virglrenderer - https://gitlab.freedesktop.org/virgl/virglrenderer/-/merge_requests/1068
  Mesa (MM) - https://gitlab.freedesktop.org/mesa/mesa/-/merge_requests/22108
  Mesa (Native Context) - https://gitlab.freedesktop.org/mesa/mesa/-/merge_requests/21658
  Mesa (Venus) - https://gitlab.freedesktop.org/mesa/mesa/-/merge_requests/23680
AMD Radeon™ RX 6000 Series

## Slide 18: Thank You and Q&A

## Slide 19
Disclaimer:
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions, and typographical errors. The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. Any computer system has risks of security vulnerabilities that cannot be completely prevented or mitigated. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
THIS INFORMATION IS PROVIDED ‘AS IS.” AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS, OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION. AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF NON-INFRINGEMENT, MERCHANTABILITY, OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY RELIANCE, DIRECT, INDIRECT, SPECIAL, OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
© 2023 Advanced Micro Devices, Inc. All rights reserved.
AMD, the AMD Arrow logo, Radeon, Ryzen and combinations thereof are trademarks of Advanced Micro Devices, Inc. Other product names used in this publication are for identification purposes only and may be trademarks of their respective companies. Linux is a trademark of Linus Torvalds and OpenCL is a trademark of Apple Inc. Windows and DirectX are the registered trademarks of Microsoft Corporation in the US and other jurisdictions.